# Overview

In this document

An Guidance sheet on safe use of the Laser Cutter

Points to consider when using this resource

This is guidance only, please adapt and amend to suit the needs of your school/machine. Please also follow the manufacture’s guidance when using your machine.

# Hazards and Precautions

Laser light

- The invisible high energy laser beam can cause severe eye damage, including blindness and serious skin burns. The doors are interlocked such that the laser beam will be disabled when the doors are opened. This will completely contain the laser beam under normal use.

- Improper use of the controls and modification of the safety features may cause serious eye injury and burns.

DO NOT modify or disable any safety features of the laser system.

DO NOT operate the laser unless all covers are in place and interlocks are working properly.

DO NOT look directly into the laser beam.

Fire

- The high intensity laser beam can produce extremely high temperatures and significant amounts of heat as the substrate material is burned away while cutting.

- Some materials can catch fire during cutting operations creating fumes and smoke inside the device.

- Dirt and debris may cause fire and a poor quality cut or mechanical component failure.

- It is important that users remain with the laser during operation to ensure that any flare-ups/ flame are properly contained and extinguished.

- Obtain the Material Safety Data Sheet (MSDS) from the material’s manufacturer when handling or processing the materials.

DO NOT use materials that are highly flammable, explosive or produce toxic by-products.

DO NOT remove material from the cutting bed before it has cooled.

DO NOT leave a laser cutter operating unattended.

ALWAYS clean up clutter, debris and flammable materials in the laser cutter after use.

ALWAYS keep a properly maintained fire extinguisher nearby.

Air contaminants

- Laser cutters will generate fumes, vapours, particulates, and metal fumes from substrate that can be highly toxic (plastics and other combustible materials).

- All laser cutter systems must be equipped with a fume exhaust system and filtration system that meets manufacturer specifications.

- These fumes or air contaminants can damage the machine and harm your health. If the air filter or exhaust system is malfunctioning, immediately stop operating the laser cutter and notify your supervisor.

- Filters must be changed regularly according to the frequency of use or as specified by the manufacturer.

DO NOT cut a material that has not been approved by the manufacturer.

DO NOT use a laser cutter with a malfunctioning exhaust system or clogged air filter.

# Sarah Pook - County Subject Inspector

Email: sarah.pook2@hants.gov.uk

For further details on the full range of services available please contact us using the following details:

Tel: 01962 874820 or email: hias.enquiries@hants.gov.uk

## HTLC professional learning moodle

Searchable course catalogue linked to the Learning Zone.

Course updates.

In-house training opportunities.

Online calendar of events.

Publications and online resources.

Bespoke consultancy services.

Link: https://hias-totara.mylearningapp.com/

# Terms and conditions

## Terms of license

Moodle+ subscribers are licensed to access and use this resource and have agreed to pay the annual subscription fee. This authority starts when the fee is paid and ends when the subscription period expired unless it is renewed. This file is for personal or classroom use only. By using it, you agree that you will not copy or reproduce this file except for your own personal, non-commercial use. HIAS have the right to modify the terms of this agreement at any time; the modification will be effective immediately and shall replace all prior agreements.

### You are welcome to:

download this resource

save this resource on your computer

print as many copies as you would like to use in your school

amend this electronic resource so long as you acknowledge its source and do not share as your own work.

### You may not:

claim this resource as your own

sell or in any way profit from this resource

store or distribute this resource on any other website or another location where others are able to electronically retrieve it

email this resource to anyone outside your school or transmit it in any other fashion.

# Text boxes

Sarah Pook

26 March 2018

Draft version

© Hampshire County Council

# Laser Cutter Guidance

HIAS MOODLE+ RESOURCE