# Portable belt sanding machine

These safety guidelines should be read in conjunction with the Portable hand-held power tools – general notes.

### Specific hazards associated with their use:

significant dust levels will be generated by this machine, potentially causing respiratory distress to both the operator and others in the vicinity. A risk assessment on dust inhalation should be carried out and LEV provided if required. RPE should also be worn if appropriate.

injury caused by the momentum generated by the moving belt – either the belt sander moving unexpectedly, or the workpiece moving if not securely clamped in place.

### Training

Students must be trained by an adult who holds a certificate of competency in the safe use of belt sanders before they are allowed to use them.

The school must keep a record of the training of individual students, including the date of training, and the specific competencies achieved, which should include:

how to position and clamp a workpiece securely and safely

how to organise and manage the position of the electrical cord

use of goggles, dust mask, secured hair and no loose fitting clothes

how and when to switch the machine on and off

awareness of any wear, damage to or misalignment of the abrasive belt.

Once a student has achieved competency with using the portable belt sanding machine, the teacher should exercise close supervision.

### Control measures

Careful consideration should be given to students using alternative processes to using this machine – the rapid removal of material that this machine is designed for may be more effectively achieved by hand planing or similar.

This machine must be connected to an effective dust extraction machine, such as an industrial vacuum cleaner fitted with a high efficiency particulate air (HEPA) filter.

The operator should have sufficient strength to withstand the pulling motion of the sanding belt if the belt becomes jammed