# Portable drilling machine

These safety guidelines should be read in conjunction with the Portable hand-held power tools – general notes.

### Specific hazards associated with their use:

loss of control due to torque generated during machine start-up, or if a drill bit jams

the chuck key being violently ejected from the chuck on start up

the drill point slipping from desired position at the start of the drilling operation

torque generated if student stops and re-starts drill, with the drill bit embedded in the workpiece

the drill breaking in use

sudden movement as drill bit cuts through material

skin contact with hot drill bit after use

contact with the sharp burr generated when drilling metals

drill bit hitting hidden electrical cable or other hidden  services when drilling into walls or floors.

### Control measures

Once a student has demonstrated competency and control with this tool, close teacher supervision should be exercised.

Use a battery powered, cordless machine if possible.

A key-less chuck should be used whenever possible – if a chuck key is used, it must be stored away from the chuck before the drill is switched on (for masonry work, an SDS drilling machine and bits are better).

Check drill size, speed and material to ensure suitable match between strength and maturity of student and operating characteristics of machine (resulting torque and feed rates required).

Use pilot holes to drill holes stage by stage if necessary.

Be aware of heat build up and potentially sharp swarf being produced if drilling metals.

Make sure the location to be drilled is pre-marked, indented, or taped to minimise the chances of the drill wandering when cutting starts.

Machine operators must de-burr metal surfaces immediately following drilling operations.

Students must always wear goggles or safety glasses. When necessary, students must wear ear defenders and a dust mask. Long hair, jewellery and any loose clothing