# Portable nail gun

These safety guidelines should be read in conjunction with the Portable hand held power tools – general notes.

### Specific hazards associated with their use:

the nail gun is a popular nailing device used in light and heavy construction. It uses the force from compressed air or an electric solenoid to drive nails through hard surfaces

compressed air powered nail guns are essentially a fire arm and must be treated accordingly

injury to eyes and face caused by unexpected break up of timber as nails are propelled from gun

injury to body parts caused by kick-back of nail gun or nails (if nail is fired against very hard materials)

penetration of body of user or other person by propelled nail in the vicinity of the nail gun operation.

### Control measures

The nail gun must only be operated by competent adults who have been trained it the safe use of the equipment.

All elements of the manufacturers safety guidelines must be adhered to.

Compressed air powered nail guns must not be operated in any area where students are present.

Nails guns must not be operated by students under the age of 18.

All adults in the vicinity of nail gun operations must wear eye protection.

Care must be taken to ensure that people are not in line with nail gun operations due to the risk of nails being fired through timber sections.

The trigger should only be held in or pressed when there is an intention to fire a nail – the trigger must not be held on to produce repeat nailing actions.

The nail gun must only be fired when it is held against a work surface.

Only use nails as specified by the manufacturer.

Nail guns must not be used by operators on ladders.

Nail guns must never be pointed in the direction of people or open space and must be carried facing down.

Operators must not place their hands behind the workpiece to support the work – the nail may penetrate through the workpiece.

Nails must not be re-used in the nail gun.

Nails may deviate whilst passing into timber due to knots, etc. Operators should be aware of this and plan the nail operation accordingly.

Compressed air nail guns must be regularly serviced by authorised and reputable specialist dealers.