# Machine maintenance record (circular saw)

| Machine: | Circular saw | Location: |  | Number: |  |
| --- | --- | --- | --- | --- | --- |
| Maintenance guidelines |
| Check machine is securely fixed in position and all electrical connections, including conduits, are soundly made. Check and ensure safe and effective operation of all electrical systems including: direct online 0v starter key operated switch foot stop switch any interlocked machine guards or cabinet plates. Check and ensure machine run-down time is less than 10 seconds. Check with most recent COSHH report for any remedial work needed to ensure effective dust extraction. Check and adjust any cover guards to prevent unauthorised access to moving parts. Check condition of blade and report any damage to teacher or technician. Check and adjust fixing of riving knife to ensure it is within 8mm of the blade Check riving knife fixing to machine body. Check suitability of table/blade access insert if fitted and adjust if needed. Check, lubricate and adjust, if necessary, blade rise and fall and tilt mechanisms. Check and ensure security of blade mounting. Check motor mounting and adjust if necessary. Check motor bearings and advise as necessary. Check and adjust motor belt drive if necessary. Check, lubricate and adjust fence clamps to ensure accurate and effective movement and clamping. Check and adjust crown guard fixings to ensure effective adjustment and clamping action. Check availability and suitability of push sticks (must be longer than 450mm). Check availability and suitability of false fence for cross-cutting and ripping operations. In all respects, the maintenance of the circular saw must comply with the Safe use of woodworking machinery: provision and use of work equipment regulations as applied to woodworking machinery – Approved Code of Practice and guidance, by Health and Safety Executive (HSE), ISBN: 978-0717616305. |
| Date | Work carried out | Comments/actions required |