# Machine maintenance record (disc sander)

| Machine: | Disc sander | Location: |  | Number: |  |
| --- | --- | --- | --- | --- | --- |
| Maintenance guidelines |
| Check the machine is securely fixed into position. Check the electrical cable, conduit and connections are free from wear and tear or damage. Check all control switches are in good working order, in particular mushroom-headed stop switches and foot, knee or hip operated stop switches. Check that all microswitches on pulley or motor cover guards operate effectively. Check that the direct online electrical 0v starter operates effectively. Check that any floor mounted stop switches are clean to ensure any moving parts are not impeded with dust or debris. Check the table and support bracket clamps are tool operated and in good working order. Check the position of the sanding table just allows the disc to rotate, clearing the abrasive grit on the disc, with a minimal gap. Check the edge guard to the periphery of the disc is less than 5mm from the disc at any point. If the disc sander is a converted woodwork lathe, check that effective arrangements for guarding the opposite end of the headstock spindle are in place. Check that all mechanical elements are correctly adjusted and lubricated. Check that the drive belts and bearings are in good working order. Check that the dust extraction system operates effectively. Check that all dust extraction hoses and connections are sound. Check that the electrical cable fitted to dust extraction unit is safely routed and secured. Check that the electrical connections, plug tops and cable fitted to dust extraction units are in good condition. Check that warning notices are clearly fixed to machine alerting users to always wear eye protection, secure loose fitting clothes, and that the machine must not be left unattended whilst the disc is still rotating. Check any other measure necessary to ensure compliance with the Provision and Use of Work Equipment Regulations (PUWER) 1998. |
| Date | Work carried out | Comments/actions required |